## Slide 1: Blue River Nutrient Enhancement Project
Brien Rose
Blue Valley Ranch
Kremmling, CO

## Slide 2: Goals
“Ecosystem based study to evaluate the role of Phosphorus (P) in Primary and Secondary production in the Lower Blue River”
  Evaluate present conditions
  Experimentally increase Phosphorus levels
  Evaluate the response of Primary and Secondary producers to increased Phosphorus levels.
  Evaluate the response of Didymo algae to increase levels of Phosphorus

## Slide 3: Relation to other projects
Kootenai River, Idaho (10x the size of the Blue River)
Gallons per Year
Added 10-34-00 Fertilizer (6,000-20,000 gallons per year)

## Slide 4: Results of Kootenai River study
Kootenai River, Idaho

## Slide 5: Total DIN Below Green Mountain
High levels of DIN
No Seasonal variations
Lower than above GMR
Below WQ standards
(Mean = 242 ug/l)
(Mean = 213 ug/l)
(Mean= 195 ug/l)
(Mean Above GMR = 233 ug/l)
(CDPHE= 1,250 ug/l)
KR=64 ug/l

## Slide 6: Total Phosphorous Below Green Mountain
-Oligotrophy Line
-EPA detection
limit)
Mostly Oligotrophic
Seasonal variations
  Higher with snowmelt
27% < than values above GMR
Mostly below standard detectability levels
(Mean = 6.6 ug/l)
(Mean = 7.9 ug/l)
(Above Green Mountain = 9.0 ug/l)
(CDPHE= 110 ug/l; Not regulated)
KR=7.9 ug/l

## Slide 7: Dissolved Phosphorous Below Green Mountain
Seasonal variations
  Higher with snowmelt
Little variation between sites
(Mean = 3.5 ug/l)
(Mean = 3.3 ug/l)
(Above Green Mountain = 3.3 ug/l)
(Unregulated)
KR=3 ug/l

## Slide 8: Soluble Reactive P Below Green Mountain
Most important variable
  “what’s available for plants”
No clear patterns
Nutrient Poor
(Mean ≈ 1.0 ug/l)
(Mean ≈ 1.0 ug/l)
(Above Green Mountain ≈ 1.0 ug/l)
(Unregulated)
KR=<1 ug/l
Goal =3 ug/l

## Slide 9: Phosphorous to nitrogen ratios
P limited Streams
P limited Streams
KR=27
Balanced TDP:TDN
Balanced P:N

## Slide 10: Importance of Phosphorus
SRP Values; Blue River ≈ 1.0
From Hill et al 2009
Blue River

## Slide 11: Injections Site and Methods
Injection Site
Control Site
Each Reach
7 Reaches
  Periphyton and invertebrates
  spaced over 7 miles
4 Water Quality Stations
  Spring Creek Rd to Trough Rd
7 Fry stations (3-4 times per year)
1 Adult Population and Condition survey
2,000-3,000 Gallons per year

## Slide 12: Study Methods—Producers
Each Reach
Periphyton
(AFDM + CL-A)
Invertebrates
(2 samples composite of3 sites )
Growth
Tiles (N=2)
Standing Crop (Rocks)
Summer/Fall
Winter/Spring
30 Day
60 Day
90 Day
Bi-Monthly
Spring
Summer
Fall

## Slide 13: Study Methods—Fish
7 Sites with Backpack Shocker
Trout Fry + Sculpin
Population
Fish >200mm
Monthly (August-November)
Growth
Raft Shocker
(2,100 m “Wild Water)
Population
Relative Weight

## Slide 14
Questions??